## Slide 1: Diffusion Imaging Quality Control with DTIPrep
Martin Styner, PhD
University of North Carolina
Neuro Image Research and Analysis Lab

## Slide 2: DWI/DTI QC
This tutorial teaches you how to do quality control (QC) of diffusion images both for DTI as well as other diffusion models (such as HARDI)
DWI/DTI QC is performed with the NA-MIC tool DTIPrep
  Can be called within Slicer
  Also stand-alone tool

## Slide 3: Dataset
For this tutorial you will need some DWI/DTI data files that can be found on this link : http://hdl.handle.net/1926/1759

## Slide 4: Diffusion Artifacts
Diffusion images are sensitive to a number of artifacts
Motion
Eddy-current distortions
Noise/SNR issues
Vibrational artifacts
Venetian blind artifacts
“unknown”…
Bad DWI’s are removed

## Slide 5: Outline
DTI QC pipeline
  Start DTIPrep
  Load DWI dataset
    Check DWI & gradient info
  Protocol for Automatic QC
  Run Automatic QC on DWI
  Final Visual QC
  Check DTI glyphs in Slicer

## Slide 6: DTIPrep
Stand alone/Slicer module
NITRC page: http://www.nitrc.org/projects/dtiprep/
  Additional manual on NITRC page
Protocol based QC
  Protocol defines all the parameters
Automatic report creation
Embed/Cropping of DWI data
  Same size images => simplifies processing
Visualization of gradient scheme

## Slide 7: Start Slicer 4
Linux/Mac users :
Launch the Slicer
executable located in
the Slicer4 directory
Windows users :
Select StartAll ProgramsSlicer4.0.1Slicer
Or launch the Slicer executable from Slicer4 directory

## Slide 8: Start DTIPrep within Slicer
Select DTIPrep
  Diffusion category
Create new module
Click “Apply”
DTIPrep starts up

## Slide 9: Workaround on Mac
Show Package Contents on Slicer
Go to Extensions => DTIPrep => cli-modules => DTIPrep

## Slide 10: DTIPrep Main Window
Toolbar
Info Window
DWI Viewers
3D Viewer

## Slide 11: Load DWI image
Click NRRD icon
File Dialog
  Select your DWI
  AdultData_DWI.nhdr
“Open”
Done with loading

## Slide 12: DWI info
Detailed
DWI
Info

## Slide 13: Gradient info in 3D
Displays gradient scheme on unit sphere
(F = File)
Check for uniformity

## Slide 14: Protocol in DTIPrep
Protocol defines parameters
Use default parameters or load prior parameter set
Select “Protocol” tab
Select “Default”
Detailed parameters
  See manual on NITRC

## Slide 15: Run QC
Select “RunByProtocol”
  Runs for a few minutes (5-15)
Checks:
Image dimensions
Gradients directions
Intensity changes across slices
Excessive motion across slices
motion and eddy current correction
Residual motion detection
Optional noise removal

## Slide 16: QC Result
Loads QC’ed DWI when finished
Detailed reporting
Directions after motion correction
Reasons for exclusion

## Slide 17: Visual QC & Save
Double click on “VC_Status”
Option to include or exclude
Often unnecessary

## Slide 18: Conclusion
DTI QC is a must
DTIPrep & Slicer provide comprehensive QC
This tutorial guided you through the “default” use of DTIPrep
Soon v1.2: Better Slicer integration, directional artifacts detection, and residual error estimation

## Slide 19: Acknowledgment
National Alliance for Medical Image Computing NIH U54EB005149
UNC: Mahshid Farzinfar, Zhexing Liu, Jean-Baptiste Berger, Clement Vachet, Cheryl Dietrich, Rachel Smith, Eric Maltbie, Yundi Shi, Aditya Gupta, Francois Budin
Utah: Guido Gerig, Sylvain Gouttard
Iowa: Hans Johnson, Joy Matsui